## Slide 1: From dumb to smarter switches in software defined networks: an overview of data plane evolution
Antonio Capone
Politecnico di Milano - ANTLab
Giuseppe Bianchi
University of Rome “Tor Vergata”
IEEE CAMAD 2014 – Athens, 1-3 December

## Slide 2: Agenda
Setting the scene: a brief intro to SDN and OpenFlow
Switches cannot remain dumb: Starting the process of data plane evolution
Not too much not too little: OpenState and statefull data planes
Applied smartness: statefull applications

## Slide 3: Setting the scene: a brief intro to SDN and OpenFlow
The future has already arrived. It's just not evenly distributed yet. [William Gibson]

## Slide 4: Classic network paradigm
Forwarding HW
OS
Distributed network functions
Forwarding HW
OS
Forwarding HW
OS
State distribution mechanism (protocols)
Router/switch/appliance

## Slide 5: Vertically integrated
Forwarding HW
OS
App
App
App
L3 Routing, L2 switching, ACL, VPNs, etc…
Control-plane
Data-plane
Closed platform!
Protocols guarantee interoperability… But what’s the drawback?
Notes: Closed platform
HW, OS and apps usually proprietary and implemented by the same vendor
Interoperability trough standard protocols

## Slide 6: Way too many standards?
Source: IETF
Notes: Way too many standard too comply with…

## Slide 8: Vendors dominated?
Source: IETF

## Slide 9: Non-standard management
Configuration interfaces vary across:
  Different vendors
  Different devices of same vendor
  Different firmware versions of same device!
SNMP fail
  Proliferation of non-standard MIBs
  Partially implemented standard MIBS
  IETF recently published a recommendation to stop producing writable MIB modules

## Slide 10: The (new) paradigm
Data-plane
Control-plane
Data-plane
Control-plane
Data-plane
Control-plane
Switch
Data-plane
Data-plane
Data-plane
Control-plane
Programmable switch
Traditional networking
Software-Defined Networking

## Slide 11: SDN architecture
Simple forwarding HW
Simple forwarding HW
Simple forwarding HW
Simple forwarding HW
Network OS
App
App
App
HW open interface
Network control API

## Slide 12: From protocols to API
HW forwarding abstraction
  low-level primitives to describe packet forwarding
Control plane API
  Network topology abstraction
  High-level access to switch programming
  Common libraries
    Host tracking
    Shortest-path
    Etc..

## Slide 13: Success keys
Low-level HW open interface
Good, extensible and possibly open-source Network OS
Open market for third-party network application developers
  Network app store
Several attempts (Active Networks, IETF ForCES), but one winner …

## Slide 14: OpenFlow
Stanford, 2008
Clean Slate research program
“With what we know today, if we were to start again with a clean slate, how would we design a global communications infrastructure?”
Is it really a clean slate approach?

## Slide 15: OpenFlow
OpenFlow Protocol (SSL/TCP)
OpenFlow controller
In-bound or out-bound
OpenFlow is actually a pragmatic approach to SDN based on a simple HW abstraction that can be implemented with current HW commercial platforms

## Slide 16: What is OpenFlow
Switch abstraction
  Match/action flow table
  Flow counters
  It doesn’t describe how this should be implemented in switches (vendor neutral !!!)
Application layer protocol
  Binary wire protocol, messages to program the flow table
Transport protocol
  TCP, TLS

## Slide 17: Flow table
Match
Actions
Counters
Forward (one or more ports)
Drop
Encapsulate and send to controller
Header rewrite
Push/pop MPLS label / VLAN tag
Queues + bitrate limiter (bit/s)
Etc..
Bytes + packets
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
L4
sport
L4
dport
VLAN
pcp
IP
ToS
Slide courtesy: Rob Sherwood

## Slide 18: Switch abstraction
OpenFlow client
Flow table (aka Forwarding Information Base)
OpenFlow controller
Software
Hardware (e.g. TCAM) or software

## Slide 19: Example
Description | Port | MAC src | MAC dst | Eth type | VLAN ID | IP Src | IP Dest | TCP sport | TCP dport | Action
L2 switching | * | * | 00:1f:.. | * | * | * | * | * | * | Port6
L3 routing | * | * | * | * | * | * | 5.6.*.* | * | * | Port6
Micro-flow handling | 3 | 00:20.. | 00:1f.. | 0x800 | Vlan1 | 1.2.3.4 | 5.6.7.8 | 4 | 17264 | Port4
Firewall | * | * | * | * | * | * | * | * | 22 | Drop
VLAN switching | * | * | 00:1f.. | * | Vlan1 | * | * | * | * | Port6, port7, port8

## Slide 20: Reactive vs Proactive
Reactive
  Start with flow table empty
  First packet of a flow sent to controller
  Controller install flow entries
  Good for stateful forwarding:
    L2 switching, dynamic firewall, resource management
Proactive
  Flow entries installed at switch boot
  Good for stateless forwarding:
    L3 routing, static firewall, etc..

## Slide 21: OpenFlow 1.0 recap
Flow table
Redirect to controller
Packet
Apply actions, forward
Drop
Notes: Too simple
Lossy abstraction

## Slide 22: Models can be perfect and clean, reality is dirty!
The match/action model can ideally be used to program any network behavior and to get rid of protocol limitations at any level
But unfortunately, with OF:
  Matches can be done only on a set of predefined header fields (Ethernet, IPv4, MPLS, VLAN tag, etc.)
  Actions are limited to a rather small set
  Header manipulation (like adding label/tags, rewriting of fields, etc.) is limited to standard schemes
As a result, OF is not really protocol independent and standards (including OF standards) are still necessary

## Slide 23: Where do OF limitations come from?
OpenFlow has been designed having in mind current specialized HW architecture for switches
Specialized HW is still fundamental in networking
  General purpose HW (CPU) and soft-switches are still 2 order of magnitude slower
  Architectures based network processors are also at least 1 order of magnitude slower
The reference HW model for OF flow tables is TCAM (Ternary Content Addressable Memory)
Flow table
(TCAM)
Redirect to controller
Packet
Actions
Drop

## Slide 24: Where do OF limitations come from?
TCAMs however are typically expensive components that are used by manufacturers only when strictly necessary
Less expensive memory components based on predefined search keys are often used for most of the common functions of a switch
OF success depends on its “vendor neutral” approach where implementations issues are completely opaque (including reuse of standard modules for e.g. MAC and IP forwarding)
Specialized ASICs are typically complex with a number of hard limitations on table types, sizes, and match depth

## Slide 25: Switches cannot remain dumb: Starting the process of data plane evolution
One man alone can be pretty dumb sometimes, but for real bona fide stupidity, there ain't nothin' can beat teamwork. [Edward Abbey]

## Slide 26: Evolution of the AL in OpenFlow: OF 1.1
Single tables are costly: all possible combinations of header values in a single long table
Solution: Multiple Match Tables (MMT)
New actions:
  Add metadata: parameters added and passed to next table
  Goto table: possibility to go to specific tables for further processing
Notes: The new group abstraction enables OpenFlow to represent a set of ports as a single entity for forwarding
packets. Different types of groups are provided, to represent different abstractions such as multicasting or
multipathing.

## Slide 27: Evolution of the AL in OpenFlow: OF 1.1
Packets of the same flow are applied the same actions unless the table entry is modified by the controller
Not good for some common and important cases (e.g. multicast, multipath load balancing, failure reaction, etc.)
Solution: Group tables
  Goto table “group table n”
  List of buckets of actions
  All or some of the buckets are executed depending on the type
Types of Group tables
  All (multicast)
  Select (multipath)
  Fast-failover (protection switching)
Notes: The new group abstraction enables OpenFlow to represent a set of ports as a single entity for forwarding
packets. Different types of groups are provided, to represent different abstractions such as multicasting or
multipathing.

## Slide 28: Evolution of the AL in OpenFlow: OF 1.1
Fast failover
Note that this is the first “stateful” behavior in the data plane introduced in OF !!!
Port A
Status monitoring
Port B
Status monitoring
Port C
Status monitoring
Port D
Status monitoring
Group table
fast failover
Action bucket 1:
FWD Port A, …
Action bucket 2:
FWD Port B, …
Action bucket 3:
FWD Port C, …
Action bucket 4:
FWD Port D, …
A
B
C
D
Notes: The new group abstraction enables OpenFlow to represent a set of ports as a single entity for forwarding
packets. Different types of groups are provided, to represent different abstractions such as multicasting or
multipathing.

## Slide 29: Evolution of the AL in OpenFlow: OF 1.2
Support for IPv6, new match fields:
  source address, destination address, protocol number, traffic class, ICMPv6 type, ICMPv6 code, IPv6 neighbor discovery header fields, and IPv6 flow labels
Extensible match (Type Length Value)
Experimenter extensions
Full VLAN and MPLS support
Multiple controllers
Notes: Type Length Value allow greater flexibility for the treatment of current and future
Protocols.
Experimentere extensions introduce dedicated fields and code points (assigned by ONF) for the implementation of extensions to the OpenFlow protocol

## Slide 30: Evolution of the AL in OpenFlow: OF 1.3
Initial traffic shaping and QoS support
  Meters: tables (accessed as usual with “goto table”) for collecting statistics on traffic flows and applying rate-limiters
Meter Table |  | 
Meter indentifier | Meter band | Counters
… | … | …
… | … | …
… | … | …
Type | Rate | Counters | Type/argument

## Slide 31: Evolution of the AL in OpenFlow: OF 1.3
More extensible wire protocol
Synchronized tables
  tables with synchronized flow entries
Bundles
  similar to transactional updates in DB
Support for optical ports

## Slide 32: Next OF: discussion started
Within ONF
Tunnel support
L4-L7 service support
Error handling
Fitness for carrier use
  Support for OAM in its various forms
Flow state (…)

## Slide 33: Next OF: discussion started
Flow state
  The capability to store / access flow metadata that persists for lifetime of flow (not just current packet)
  Potential to enable a variety of new capabilities:
    Fragment handling without reassembly
    Relation between bidirectional flows (e.g., RDI)
    Autonomous flow learning + flow state tracking
    MAC learning
    TCP proxy
  Hierarchies of flows
    e.g. FTP control / data, all belonging to a user, etc.
[MAC13] Ben Mack-Crane, “OpenFlow Extensions”, US Ignite ONF GENI workshop, Oct 2013

## Slide 34: Also abstraction “involutions” (?): Typed tables
“A step back to ensure wider applicability”
A third way between reactive and proactive
Pre-run-time description of switch-level “behavioral abstraction” (tell to the switch which types of flowmods will be instantiated at run time)
Limit types supported according to HW type
ONF Forwarding Abstractions WG
OpenFlow 1.0
Typed tables patterns: Forwarding Elements (F:E.)
Constrained OpenFlow 1.1
Layer 3 IPv4
Stateless Generic Tunnel
Statefull Generic Tunnel
802.1D Forwarding
(…)

## Slide 35: Further flexibility limitations due to specialized HW
OF introduced the MMT model but does not mandate the width, depth, or even the number of tables
OF allows the introduction of new match fields through a user-defined field facility
But existing switch chips implement a small (4–8) number of tables whose widths, depths, and execution order are set when the chip is fabricated.
This severely limits flexibility through specialized chips:
  Chip for core routers: large 32-bit IP longest matching table and a small 128 bit ACL match table
  Chip for enterprise router: small 32-bit IP table and large ACL table, with an additional MAC address match tables
[BOS13] P. Bosshart, G. Gibb, H.-S. Kim, G. Varghese, N. McKeown, M. Izzard, F. Mujica, and M. Horowitz, “Forwarding metamorphosis: Fast programmable match-action processing in hardware for sdn”, in ACM SIGCOMM 2013.

## Slide 36: Reconfigurable Match Tables (RMT)
Recent proposal by McKeown, Varghese et al. [BOS13]
RMT
  Field definitions can be altered and new fields added
  Number, topology, widths, and depths of match tables can be specified, subject only to an overall resource limit on the number of matched bits
  New actions may be defined
  Arbitrarily modified packets can be placed in specified queues, for output at any subset of ports, with a queuing discipline specified for each queue.
[BOS13] P. Bosshart, G. Gibb, H.-S. Kim, G. Varghese, N. McKeown, M. Izzard, F. Mujica, and M. Horowitz, “Forwarding metamorphosis: Fast programmable match-action processing in hardware for sdn”, in ACM SIGCOMM 2013.

## Slide 37: Reconfigurable Match Tables (RMT)
[BOS13] P. Bosshart, G. Gibb, H.-S. Kim, G. Varghese, N. McKeown, M. Izzard, F. Mujica, and M. Horowitz, “Forwarding metamorphosis: Fast programmable match-action processing in hardware for sdn”, in ACM SIGCOMM 2013.
Programmable parser
Global states
Header re-write with very long instruction word (VLIW)
Configurable queues
Physical flexible architecture on chip

## Slide 38: All the way down to programmability: P4
Recent “strawman proposal” by McKeown, Rexford et al. [BOS13b]
[BOS13b] P. Bosshart, D. Daly, M. Izzard, N. McKeown, J. Rexford, D. Talayco, A. Vahdat, G. Varghese, D. Walker, “P4: Programming protocol-independent packet processors,” arXiv:1312.1719.
Towards real protocol independence:
  No predefined fields, but reconfigurable fields
  Protocol independence, switches not be tied to any specific network protocols
  Target independence: flexible packet-processing functionality independently of the specifics of the underlying hardware.
Advanced “configurability”

## Slide 39: All the way down to programmability: P4
Configurability achieved with a programming language describing parsing and control
[BOS13b] P. Bosshart, D. Daly, M. Izzard, N. McKeown, J. Rexford, D. Talayco, A. Vahdat, G. Varghese, D. Walker, “P4: Programming protocol-independent packet processors,” arXiv:1312.1719.
Programs are “compiled” according to the specific specialized HW

## Slide 40: Protocol Oblivious Forwarding (POF)
Removing/neglecting constraints on general HW can lead to extreme flexibility of a clean slate approach (not in the OF evolution track)
POF proposal by Huawei [SON13]
POF makes the forwarding plane totally protocol-oblivious
The POF FE has no need to understand the packet format.
POF FE execute instruction of its controller to:
  extract and assemble the search keys from the packet header,
  conduct the table lookups,
  execute the associated instructions (in the form of executable code written in FIS or compiled from FIS).
[SON13] H. Song, “Protocol-oblivious forwarding: Unleash the power of SDN through a future-proof forwarding plane, HotSDN ’13. ACM, 2013, pp. 127–132.

## Slide 41: Tiny programs in the packets
Taking programmability to the extreme …
Remember “active networks” …
[JEY13] V. Jeyakumar, M. Alizadeh, C. Kim, and D. Mazieres, “Tiny packet programs for low-latency network control and monitoring,”. HotSDN ’13

## Slide 42: Deeply Programmable Networks (FLARE)
Fully programmable control plane
Fully programmable data plane
Flexible and extensible API for both planes
Experimental implementation
Aki Nakao, FLARE Project, NakaoLab, The university of Tokyo.

## Slide 43: Not too much not too little: OpenState and stateful data planes
Too clever is dumb.
[Ogden Nash]

## Slide 44: Looking for the “right” abstraction
Programmability and real world viability
  High levels of (deep) programmability in the data and control planes since ages
    Active Networks
    IETF ForCES
Keywords for success:
  Pragmatism
  Compromise
  “right” mix of programmability: right level of abstraction
    Many wonderful programmable platforms buried in the “lab world”

## Slide 45: Remember: OF meant to be a compromise [original quotes: from OF 2008 paper]
Best approach: “persuade commercial name-brand equipment vendors to provide an open, programmable, virtualized platform on their switches and routers”
  Plainly speaking: open the box!! No way…
Viable approach: “compromise on generality and seek a degree of switch ﬂexibility that is
  High performance and low cost
  Capable of supporting a broad range of research
  Consistent with vendors’ need for closed platforms.

## Slide 46: OF forces separation of data and control
Logically-centralized control
DUMB!
SMART!
Events from switches
Topology changes,
Traffic statistics,
Arriving packets
Commands to switches
(Un)install rules,
Query statistics,
Send packets

## Slide 47: Centralized Control: pros and cons
PROS:
  Central view of the network as a whole
    Network states, etc
  One-click network config/deploy
    Platform agnosting switch API is key - e.g. OpenFlow forwarding abstraction
CONS:
  Control latency!!!
    O(second) 1s = 300M packets lost @ 100 gbps
  Signalling overhead
Great idea for network-wide states and «big picture» decisions
Poor idea for local states/decision, (way!) better handled locally
(less delay, less load)

## Slide 48: Distributed controllers the «common» way to address such cons
A non-solution!
still slow path latency!!
Proprietary controller extensions?
Back to Babel?
«true» fast path solution: update forwarding rules in 1 packet time – 3 ns @ 40B x 100 Gbps
3 ns = 60cm signal propagation…

## Slide 49: Our vision
SMART!
SMART!
Events from switches & central rule updates
Restricted to those of interest
for GLOBAL decisions
Inject “switch control programs”
Change forwarding behavior as
specified by “this program” IF
(local) events occur
Decision on how network should operate remains at the controller (SDN vision)
But “execution” of forwarding plane updates can be locally delegated
Local processing: Ultra low Latency: o(nanosec) versus o(sec)
Local states: lower signalling

## Slide 50: What is missing in the picture
Behavioral Description
src=1.2.*.*, dest=3.4.5.*  drop
src = *.*.*.*, dest=3.4.*.*  forward(2)
src=10.1.2.3, dest=*.*.*.*  send to controller
«generic» forwarding device
Any vendor, any size, any HW/SW platform…
OF forwarding abstraction insufficient!!
Platform-agnostic stateful processing: how to?
«repurposed» device

## Slide 51: Easier said than done
We need a switch architecture and API which is…
  High performance: control tasks executed at wire-speed (packet-based events)
  Platform-independent: consistent with vendors’ needs for closed platforms
  Low cost and immediately viable: based on commodity HW
Apparently, far beyond OpenFlow switches…
Our (perhaps surprising?) finding: much closer to OF than expected!!

## Slide 52: Our findings at a glance
Any control program that can be described by a Mealy (Finite State) Machine is already (!) compliant with OF1.3
MM + Bidirectional flow state handling requires minimal hardware extensions to OF1.1+
Proof of concept HW and SW implementation

## Slide 53: Our approach: OpenState easier understood via a running example: port knocking
[CCR14] G. Bianchi, M. Bonola, A. Capone, C. Cascone, “OpenState: programming platform-independent stateful OpenFlow applications inside the switch”, ACM Computer Communication Review, vol. 44, no. 2, April 2014.
[ARX14] G. Bianchi, M. Bonola, A. Capone, C. Cascone, S. Pontarelli, “Towards Wire-speed Platform-agnostic Control of OpenFlow Switches”, available on ArXiv, 2014.

## Slide 54: Remember OF match/action API
Multiple flow tables
since OF version 1.1
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Matching
Rule
Action
FORWARD TO PORT
ENCAPSULATE&FORWARD
DROP
…
Extensible
Vendor-implemented
Programmabile logic
Pre-implemented matching engine

## Slide 55: Background: Port Knocking firewall knock «code»: 5123, 6234, 7345, 8456
IPsrc=1.2.3.4
Port=5123
Drop(); 1.2.3.4  1° knock OK
IPsrc=1.2.3.4
Port=6234
Drop(); 1.2.3.4  2° knock OK
IPsrc=1.2.3.4
Port=7345
Drop(); 1.2.3.4  3° knock OK
IPsrc=1.2.3.4
Port=8456
Drop(); 1.2.3.4  OPEN port SSH
IPsrc=1.2.3.4
Port=22
Forward()

## Slide 56: Port Knocking @ controller
IPsrc=any
Port=any
DROP
controller
Encapsulate & forward ALL packets of ALL flows
IPsrc=any
Port=any
Maintain Knock state per flow
When knock sequence
finalized, add entry
<Ipsrc, port=22; forward>
Lots of overhead!!
Needed as no «knock» state handled in switch

## Slide 57: «Abstract» description for port knocking: Mealy Machine
DEFAULT
Stage 1
Stage 2
Stage 3
OPEN
Port=6234
Drop()
Port!=6234
Drop()
Port!=5123
Drop()
Port=5123
Drop()
Port=7345
Drop()
Port=8456
Drop()
Port!=7345
Drop()
Port!=8456
Drop()
Port=22
Forward()
Port!=22
Drop()

## Slide 58: Can transform in a flow table? Yes: MATCH: <state, port>  ACTION: <drop/forward, state_transition> Plus a state lookup/update
state
event
DEFAULT
STAGE-1
Port=5123
Port=6234
STAGE-2
STAGE-3
Port=7345
Port=8456
OPEN
Port=22
OPEN
*
Port=*
Port=*
Match fields
Actions
action
Next-state
drop
drop
STAGE-1
STAGE-2
drop
drop
STAGE-3
OPEN
forward
OPEN
drop
drop
OPEN
DEFAULT
IPsrc
Port
Metadata: State-label
State DB
State DB
IpsrcOPEN
Ipsrc: ??

## Slide 59: Putting all together
Flow key
state
IPsrc= … …
Ipsrc= … …
… … …
… … …
IPsrc=1.2.3.4
IPsrc=5.6.7.8
STAGE-3
OPEN
IPsrc= no match
DEFAULT
IPsrc= … …
State Table
… … …
IPsrc=1.2.3.4
Port=8456
1) State lookup
state
event
DEFAULT
STAGE-1
Port=5123
Port=6234
STAGE-2
STAGE-3
Port=7345
Port=8456
OPEN
Port=22
OPEN
*
Port=*
Port=*
XFSM Table
Match fields
Actions
action
Next-state
drop
drop
STAGE-1
STAGE-2
drop
drop
STAGE-3
OPEN
forward
OPEN
drop
drop
OPEN
DEFAULT
IPsrc=1.2.3.4
Port=8456
STAGE-3
2) XFSM state transition
IPsrc=1.2.3.4
Port=8456
OPEN
3) State update
write
Write: OPEN
1 «program» XFSM table for all flows
(same knocking sequence)
N states, one per (active) flow

## Slide 60: Proof of concept
SW implementation:
  Trivial modifications to SoftSwitch
  Public domain
HW implementation:
  5 clock (2 SRAM read + 2 TCAM + 1 SRAM write)
  10 Gbps just requires 156 MHz clock TCAM, trivial
  Optimization in progress (pipelining) for 100 Gbps.

## Slide 61: Cross-flow state handling
MACdst
MACsrc
Flow key
state
48 bit MAC addr
Port #
lookup
State Table
MACdst
MACsrc
Flow key
state
48 bit MAC addr
Port #
update
State Table
state
event
Port#
*
action
Next-state
forward
In-port
XFSM Table
DIFFERENT lookup/update scope
Field 1
Field 2
Field N
Flowkey selector
Read/write signal
Yes but what about MAC learning, multi-port protocols (e.g., FTP), bidirectional flow handling, etc?

## Slide 62: Current challenge Prove programmability of complex functions
DONE:
Port Knocking
MAC learning
Label/address advertisement learning
Reverse Path Forwarding
Flow-consistent Load Balancing
DDoS multi-stage flow marking
…
Our challenge: towards an open «flow processor»?
CHALLENGE:
IDS/DPI
TCP flow processing
Monitoring
…
Need new «actions»
Need extra logic (full XFSM)
All (!) otherwise not possible without explicit controller’s involvement or custom distrib. control…

## Slide 63: Aftermath
Control intelligence in devices seems possible
  Via Platform-independent abstraction
  Retaining high speed & scalability
  As «small» OpenFlow extension (?!)
TCAM as «State Machine processor»
  Now Mealy Machines
  Currently working on full XFSM extension
Rethinking control-data plane SDN separation?
  Control = Decide! Not decide+enforce!

## Slide 64: Applied smartness: stateful applications
There are science and the applications of science, bound together as the fruit of the tree which bears it. [Louis Pasteur]

## Slide 65: openstate-sdn.org
Switch: ofsoftswitch13; Controller: Ryu

## Slide 66: Forwarding Consistency
Ensure consistency in forwarding decisions for packets of a same transport layer flow
Example: LAG @Internet Exchange Point
Example: Server Load Balancer

## Slide 67: Forwarding Consistency
One to Many:
Intra-flow state handling
Many to One:
Cross-flow state handling
Many to Many:
Inter-stage cross-flow state handling

## Slide 68: Forwarding Consistency: One to Many
The first packet of a TCP connection coming from the input port is sent to one of many possible output ports.
All the next packets of the same TCP connection must be forwarded on the same selected port.

## Slide 69: Forwarding Consistency: One to Many
OpenFlow solution: the controller is in charge of states management.
controller
First packet of each new TCP connection is sent to the controller in order to:
-select an output port (e.g. randomly) and forward the packet
-install a flow entry for subsequent packets

## Slide 70: Forwarding Consistency: One to Many
Controller is not involved!
OpenState solution:
the switch itself handles connection’s state.
A flow is identified by [IP_SRC,IP_DST,TCP_SRC,TCP_DST]
FLOW STATE: output port
First packet of each new TCP connection is sent to the Group Table in order to:
select an output port randomly
store the selected port in the State Table for subsequent packets

## Slide 71: Forwarding Consistency: One to Many
#
action
Next-state
Flow key
State
State Table
IP_src=10.0.0.1
1) State lookup
state
event
DEF.
1
In-port=1
In-port=1
2
3
In-port=1
In-port=1
*
In-port=2
*
*
In-port=3
In-port=4
XFSM Table
Match fields
Actions
action
Group(1)
Forward(2)
Forward(3)
Forward(4)
Forward(1)
Forward(1)
Forward(1)
2) XFSM state transition
2
4) State update
write
In this case the state is set in the group table
Random Group Entry
Lookup Scope: IP_src, IP_dst, TCP_src,TCP_dst
Update Scope: IP_src, IP_dst, TCP_src,TCP_dst
IP_dst=10.0.0.2
TCP_src=2500
TCP_dst=80
IP_src=10.0.0.1
IP_dst=10.0.0.2
TCP_src=1000
TCP_dst=80
… …
… …
… …
… …
IP_src=10.0.0.1
IP_dst=10.0.0.2
TCP_src=3000
TCP_dst=80
*
*
*
*
1
… …
3
DEFAULT
IP_src=10.0.0.1
IP_dst=10.0.0.2
TCP_src=2500
TCP_dst=80
DEFAULT
Group Entry
Buckets
Entry 1
Forward(2)
1
Forward(3)
2
Forward(4)
3
Group Table
IP_dst=10.0.0.2
IP_src=10.0.0.1
TCP_src=2500
TCP_src=80
2
IP_src=10.0.0.1
IP_dst=10.0.0.2
TCP_src=2500
TCP_dst=80

## Slide 72: Forwarding Consistency: Many to One
Forwarding consistency must be ensured according to packets received in the reverse direction.
The first packet of a TCP connection coming from one of the many input ports is forwarded on the only output port.
All packets of the reverse flow of the same TCP connection must be forwarded on the same ingress port.

## Slide 73: Forwarding Consistency: Many to One
OpenFlow solution:
the controller is in charge of states management.
controller
First packet of each new TCP connection is sent to the controller in order to:
-forward the packet
-install a flow entry for reverse flow’s packets

## Slide 74: Forwarding Consistency: Many to One
Cross-flow state
Controller is not involved!
OpenState solution:
the switch itself handles connection’s state.
First packet of each new TCP connection is forwarded and the input port is stored to forward response packets
A flow is identified by [IP_SRC,IP_DST,TCP_SRC,TCP_DST]
FLOW STATE: input port

## Slide 75
Next-state
action
Flow key
State
State Table
IP_dst=10.0.0.100
1) State lookup
state
event
1
2
In-port=4
In-port=4
3
*
In-port=4
In-port=1
*
In-port=2
*
In-port=3
XFSM Table
Match fields
Actions
Forward(1)
Forward(2)
Forward(3)
Forward(4)
Forward(4)
Forward(4)
2) XFSM state transition
1
3) State update
write
Communication Host -> Server
Lookup Scope: IP_src, IP_dst,TCP_src,TCP_dst
Update Scope: IP_dst,IP_src,TCP_dst,TCP_src
IP_src=10.0.0.1
TCP_src=2500
TCP_dst=80
IP_dst=10.0.0.2
IP_src=10.0.0.200
TCP_src=80
TCP_dst=1000
… …
… …
… …
… …
… …
… …
… …
… …
*
*
*
*
2
… …
… …
DEFAULT
IP_src=10.0.0.1
IP_dst=10.0.0.100
TCP_src=2500
TCP_dst=80
DEFAULT
IP_src=10.0.0.100
IP_dst=10.0.0.1
TCP_src=80
TCP_dst=2500
1
-
-
-
1
2
3
IP_dst=10.0.0.100
IP_src=10.0.0.1
TCP_dst=2500
TCP_src=80
IP_src=10.0.0.100
IP_dst=10.0.0.1
TCP_src=2500
TCP_dst=80
DIFFERENT lookup/update scope
Forwarding Consistency: Many to One

## Slide 76: Forwarding Consistency: Many to One
Communication Server -> Host
Lookup Scope: IP_src, IP_dst,TCP_src,TCP_dst
Update Scope: IP_dst,IP_src,TCP_dst,TCP_src
Next-state
action
Flow key
State
State Table
IP_src=10.0.0.100
1) State lookup
state
event
1
2
In-port=4
In-port=4
3
*
In-port=4
In-port=1
*
In-port=2
*
In-port=3
XFSM Table
Match fields
Actions
Forward(1)
Forward(2)
Forward(3)
Forward(4)
Forward(4)
Forward(4)
2) XFSM state transition
IP_dst=10.0.0.1
TCP_src=2500
TCP_dst=80
IP_dst=10.0.0.2
IP_src=10.0.0.200
TCP_src=80
TCP_dst=1000
IP_dst=10.0.0.1
IP_src=10.0.0.100
TCP_scr=80
TCP_dst=2500
… …
… …
… …
… …
*
*
*
*
2
1
… …
DEFAULT
IP_src=10.0.0.1
IP_dst=10.0.0.100
TCP_src=2500
TCP_dst=80
1
-
-
-
1
2
3

## Slide 77: Forwarding Consistency: Many to Many
Combining the first two, we want here to load balance on the output ports while doing reverse path forwarding on the input port
The first packet of a TCP connection coming from one of the many input ports is forwarded to one of many possible output ports.
All the next packets of the same TCP connection must be forwarded on the same selected output port, while all packets of the reverse flow of the same TCP connection must be forwarded on the same ingress port.

## Slide 78: Forwarding Consistency: Many to Many
OpenState solution
A flow is identified by [IP_SRC,IP_DST,TCP_SRC,TCP_DST]
Two states are needed for each bidirectional flow:
FLOW STATE 1: output port
FLOW STATE 2: input port
For each first packet of each new TCP connection:
packet is forwarded to a random output port
the selected output port is stored in the State Table 0
the input port is stored in the State Table 1

## Slide 79: Forwarding Consistency: Example Results
Results will show the average value of the time required by 1000 TCP SYN packets to cross the switches at increasing rate.
Switch: ofsoftswitch13; Controller: Ryu
One-to-Many
OpenFlow
ofsoftswitch13
OpenFlow
Open Vswitch
OpenState
ofsoftswitch13
Many-to-One
OpenFlow
ofsoftswitch13
OpenFlow
Open Vswitch
OpenState
ofsoftswitch13
Many-to-Many
OpenFlow
ofsoftswitch13
OpenFlow
Open Vswitch
OpenState
ofsoftswitch13

## Slide 80: Fault Tolerance
Ensure the network failure resiliency, quickly readapting the routing after a failure
Fundamental function in any network (telco operators, data centers)
Weak support in OpenFlow

## Slide 81: Fault Tolerance
OpenFlow
Fast failover: local reroute based on port states (Group table)
But what if a local reroute in not available ???

## Slide 82: Fault Tolerance
controller
Obviously it is always possible to rely on the controller to:
forward the packet on the backup path
install flow entries for the backup path
OpenFlow

## Slide 83: Fault Tolerance in OpenState
With OpenState the switch itself can react to the fault
PKT
PKT
TAG
Proposed solution:
Faults are signaled using the same data packets
Packets are tagged and sent back
Packets are sent back until matched against a node able to respond to that fault

## Slide 84: Fault Tolerance
OpenState
A DETOUR is enabled based on the specific failure without constraints
Backup paths can be pre-computed and installed by the controller (traffic engineering and quality/congestion control)
The controller is entitled to restore the primary path once the fault has been resolved
[CAP14] A. Capone, C. Cascone, A. Nguyen, B. Sansò, “Detour Planning for Fast and Reliable Failure Recovery in SDN with OpenState”, available on ArXiv, Nov. 2014.

## Slide 85: Fault Tolerance: Fault Reaction Example
PKT
PKT
PKT
TAG
PKT
TAG
PKT
TAG
PKT
PKT
TAG
PKT
PKT
Redirect Node:
FLOW STATE = DEF
Detect Node:
GLOBAL REGISTERS = 00
20
01
DEF
20
i
DEF
20
STATE
TRANSITION!
FLAG SETUP
Fault_ID=20
TAG = FAULT_ID = 20
TAG = STATE = 20
OpenState

## Slide 86: Fault Tolerance: Example on larger network
Primary node
19
13
17
16
15
Detect node
Forward-back node
Redirect node
Detour node

## Slide 87: Fault Tolerance: Exampe Results
OpenFlow:
Controller applications
OpenState:
Precomputed backup paths

## Slide 88: Thanks
OpenState: openstate-sdn.org
EU project BEBA (web site available soon) – follow us!
This slide-set soon available on OpenState web site!
Antonio Capone
Email: antonio.capone@polimi.it
Giuseppe Bianchi
Email: giuseppe.bianchi@uniroma2.it